## Slide 1: Extending Utah Energy Balance Snowmelt Model to Glacial Melt Calculations in HIMALA project
David Tarboton
Avirup Sen Gupta
Utah State University
http://www.engineering.usu.edu/dtarb dtarb@usu.edu

## Slide 2: Overview
Adapting UEB Model for HIMALA
Process representations
Input/Output refactoring
Langtang Khola Example

## Slide 3: Challenges for Himala
Extending UEB to glaciers
  Process physics
  Melt from debris covered glaciers
  Albedo and substrate as an input
Interfaces (input and output file formats)
  Coordination of UEB output with BASINS and GeoSFM

## Slide 4: Utah Energy Balance Model Overview
Physically based calculation of snow energy balance.
  Predictive capability in changed settings
  Strives to get sensitivities to changes right
Simplicity. Small number of state variables and adjustable parameters.
  Avoid assumptions and parameterizations that make no difference
Transportable. Applicable with little calibration at different locations.
Match diurnal cycle of melt outflow rates
Match overall accumulation and ablation for water balance.
Distributed by application over a spatial grid.
Effects of vegetation on interception, radiation, wind fields

## Slide 5: Processes in the Utah Energy Balance Snowmelt Model at a point
Fluxes dependent on
surface temperature
Qhs(Ta,Ts) Qes(ea,Ts) Qles(Ts)
Above Canopy Inputs
Qsi ea Ta Precip Wind
Qsib Qsid Qli , Qp,
τbQsib τdQsid τd Qli Qps
Thermally active ground layer
Canopy Variable
Water Equivalent Wc
Leaf Area Index LAI
Direct radiance transmittance τb
Diffuse radiance transmittance τd
Q
Soil
Snow
De
Qm
Qg
Qhc(Ta,Tc) Qec(ea,Tc) Qlec(Tc)
Qlec (Tc)
Fluxes dependent on Canopy temperature
Energy Content Us
Water Equivalent Ws
David Tarboton: http://www.engineering.usu.edu/dtarb

## Slide 6: UEB Model Structure
State Equations
  Surface mass and energy balance (beneath the canopy)
Canopy mass and energy balance
State Variables
    Surface snow water equivalent, Ws
    Internal energy of the surface snowpack, Us
    Canopy snow water equivalent, Wc
Notes: Enhanced UEB model is also a parsimonious model
It has only three state variables namely, ………. and has two layers.
Rate of change of internal energy of snow is

## Slide 7: Numerical Approach
Predictor
  t
Corrector
True
Corrector
Predictor
t
W
t

## Slide 8: Focus on parameterizations of
Glacier ice melting - new
Snow surface temperature
[Refreezing at the surface]
Spatial variability - grid or [subgrid parameterization]
Vegetation

## Slide 9: Glacier melt representation
Substrate type may be
  0 bare ground (or vegetated)
  1 clean glacier ice
  2 dirty glacier ice
  3 accumulation zone (model not run)
Glacier ice
UEB Layer
Seasonal snow
Seasonal Snow accumulation and melt
Glacier Ice Melting
Seasonal snow off
Albedo may optionally be a spatially and time varying input
Substrate albedo specified
Does not model glacier ice flow

## Slide 10: Snow surface temperature
Heat diffusion into a semi-infinite medium with periodic (diurnal) boundary conditions
Solution
where, k = /C
where, d = (2k)1/2
Modified Force-Restore (MFR)

## Slide 11: Evaluation/Validation of SWE
MFR
EQG
Central Sierra Snow Lab (1986)

## Slide 12: Evaluation/Validation of Internal Energy
Cache Valley, Utah, USA (1993)

## Slide 13: Vegetation Component
To improve snowmelt modeling capability to account for the effects of forest canopy on the accumulation, sublimation and melting of snow
  Canopy Radiation Transmission
  Below and above canopy turbulent energy exchanges
  Canopy Snow Interception
Bypassed when Leaf Area Index (LAI) is 0 as over glaciers and bare ground, but important in forested areas

## Slide 14: Canopy Radiation Transmission
Shortwave (Solar) Radiation Fractions
Longwave Radiation Fractions
Q
f
1
Q
Canopy
Surface
Q
Q
f
2
Q
f
3
Q
Partitioning accounting for
Vegetation transmittance (LAI)
Reflection, absorption, back scatter
Surface and vegetation albedo
Applied to both shortwave and longwave radiation (with different coefficients and longwave black body emissions)
Mahat, V. and D. G. Tarboton, (2012), "Canopy radiation transmission for an energy balance snowmelt model," Water Resour. Res., 48: W01534, http://dx.doi.org/10.1029/2011WR010438.

## Slide 15: Canopy Wind and Turbulent Fluxes Adaptation of two source land surface model for snow (Norman et al., 1995)
Norman, J. M., W. P. Kustas and K. S. Humes, (1995), "Source approach for estimating soil and vegetation energy fluxes in observations of directional radiometric surface temperature," Agricultural and Forest Meteorology, 77(3-4): 263-293, http://dx.doi.org/10.1016/0168-1923(95)02265-y.

## Slide 16: Canopy Interception Processes
    The rate of snow interception (m hr-1)
    The rate of snow mass unloading (m hr-1)
    Melt from the canopy (m hr-1)
    Sublimation of canopy snow (m hr-1)
Notes: The canopy snow interception processes algorithms we developed and added to the UEB model are
hf= latent heat of fusion

## Slide 17: Validation/Evaluation of Vegetation Component
T.W. Daniel Experimental Forest, Logan, Utah, USA
Mahat, V. and D. G. Tarboton, (2012), "Canopy radiation transmission for an energy balance snowmelt model," Water Resour. Res., 48: W01534, http://dx.doi.org/10.1029/2011WR010438.
Notes: This slide shows the modeled vs measured SWE for different vegetation for three years.
We are focusing on the melt period where effects of interception is less.
This result suggests that the model is able to capture the snowmelt rate that is sensitive to different forest type and leaf density.

## Slide 18: UEB Grid Implementation
Model run separately at each active grid cell
Melt outputs aggregated for subwatersheds
Structured File based IO for linking with BASINS and GeoSFM
ASCII for non spatial data
NetCDF for geospatial data

## Slide 19: Variable types
Spatially constant and constant in time (SCTC) such as model parameters.
Spatially constant but time varying (SCTV) such as an input quantity for which there is not information about spatial variability.
Spatially variable but constant in time (SVTC) such as slope, aspect and substrate type.
Spatially variable and variable in time (SVTV) such as air temperature and Precipitation that vary in time and space.

## Slide 20: Spatially Variable Input Layers (SVTC)
Elevation
Substrate Type
Albedo
Aspect
Slope
Subwatersheds
Others ...

## Slide 21: Space time inputs (SVTV)
x
y
t
Precipitation
Air temperature
Solar Radiation
etc.
As 3D NetCDF files

## Slide 22: UEB Grid Implementation Model run through time for each active grid cell
Time Outputs
Spatial Outputs

## Slide 23: File-Based Input-output system
Overall control file
Input Files
Watershed file
Provides watershed ID for each grid from the NetCDF file
Site Initial file
Provides site and initial condition values, or points to 2-D NetCDF files where these are spatially variable
Provides start, end and time step, and info. on time varying inputs as either from text file for domain, from 3-D NetCDF file where spatially variable, or constant for all time
Parameter file
Provides parameter Values
Input Control file
2-D NetCDF files
Provides spatially variable site and initial condition values
3-D NetCDF files
Provides input variables for each time step and each grid point
Time series text file
provides input variables for each time step and assumes a constant value for all the grid points
Point detail text file
Aggregated Output Control
Holds list of variables for which aggregated output is required
3-D NetCDF files
Holds a single output variable for all time steps and for entire grid.
Aggregated Output text file
Holds aggregated output
Output Control file
Indicates which variables are to be output and the file names to write outputs.
Holds all output variables for all time steps for a single grid point
Output Files

## Slide 24: Preliminary Langtang Khola Results for evaluation/validation

## Slide 25: Substrate Type
Type of beneath snow substrate encoded as (0 = Ground/Non Glacier, 1=Clean Ice/glacier, 2= Debris covered ice/glacier, 3= Glacier snow accumulation zone)

## Slide 28: Substrate Albedo

## Slide 29: Examination of results at 4 points
A
B
C
D

## Slide 30: Input Air Temperature
Input Air Temperature adjusted from measurement at the outlet using elevation and a lapse rate (6 C/km)
Concern over whether the jump is correct

## Slide 31: Solar Radiation
Differences due to slope and aspect
Values greater than solar constant due to energy being modeled per unit horizontal area
A is west facing 45o
Slope area As
Horizontal area Ai
Qsi = Io Tf As/Ah

## Slide 32: Precipitation
Input Precipitation measured at outlet assumed the same everywhere
Air Temperature C
Snow Fraction

## Slide 33: Snow Water Equivalent
This is seasonal snow above the glacier surface that accumulates due to modeled seasonal snowfall

## Slide 34: Melt Outflow
This is total modeled outflow that includes snowmelt, rainfall when there is no seasonal snow and glacier melt

## Slide 35: Total and Glacier Melt at B (Clean Glacier)

## Slide 36: Cumulative Melt July 2001
Total melt including snowmelt, rainfall and glacier melt accumulated over the month of July 2001
Average 0.297 m
Complete Watershed (Langtang Khola) July 2001 flow is 11.6 m3/s corresponding to 0.47 m over glacier area or 0.088 m over full area

## Slide 37: Yala Cumulative Melt
Total melt including snowmelt, rainfall and glacier melt accumulated over the month of July 2001
Average 0.31 m
Complete Watershed (Langtang Khola) July 2001 flow is 11.6 m3/s corresponding to 0.47 m over glacier area or 0.088 m over full area

## Slide 38: Langtang Khola Cumulative Melt
Total melt including snowmelt, rainfall and glacier melt accumulated over the month of July 2001
Average 0.287 m
Complete Watershed (Langtang Khola) July 2001 flow is 11.6 m3/s corresponding to 0.47 m over glacier area or 0.088 m over full area

## Slide 39: Steps in ongoing work
Vectorize input and output to improve efficiency
Validation, evaluation and sensitivity analysis
  Run using NASA Modern Era-retrospective Analysis for Research and Application (MERRA) downscaled data
  Run over other watersheds comparing to streamflow measurements
  Run in the BASINS framework to evaluate/validate integration

## Slide 40: Collaborations
ICIMOD, Kathmandu University, Aquaterra (others)
ICIMOD
  help with local data for evaluation
  help with facilitating applicability
Kathmandu University
  glacier melt mechanisms and glacier processes
  Local data and knowledge
Aquaterra
  BASINS integration

## Slide 41: Summary/Conclusions
UEBGrid is ready for integration with BASINS
  Issues that arise will need to be addressed
UEBGrid is producing glacier melt outputs that need evaluation and examination
  to validate model functioning
  to validate input data